## Slide 1
Fiber network issues (SCL)
January’19 to 9th March, 2019
Technology Operations

## Slide 2
Fiber Incident Count & Outage
Chart: Incident Count
| Wk-1 | Wk-2 | Wk-3 | Wk-4 | Wk-5 | Wk-6 | Wk-7 | Wk-8 | Wk-9 | Wk-10
C-1 | 2 | 2 | 2 | 1 | 2 | 1
C-2 | 1 | 1 | 2 | 1 | 2 | 1 | 2 | 1
C-3 | 3 | 9 | 9 | 2 | 7 | 6 | 9 | 14 | 8 | 8
No Impact | 9 | 5 | 14 | 19 | 12 | 17 | 12 | 19 | 16 | 15
Grand Total | 13 | 16 | 26 | 25 | 21 | 25 | 23 | 34 | 26 | 25
Chart: MTTR Trend
| C-1 | C-2 | C-3 | No Impact
Wk-1 | 0.14167 | 0.14745 | 0.15756
Wk-2 | 0.072569 | 0.084491 | 0.13319
Wk-3 | 0.088889 | 0.020833 | 0.097377 | 0.19335
Wk-4 | 0.011111 | 0.04375 | 0.049653 | 0.10493
Wk-5 | 0.14653 | 0.022917 | 0.18899 | 0.1923
Wk-6 | 0.029167 | 0.08044 | 0.20478
Wk-7 | 0.12222 | 0.12477 | 0.11672
Wk-8 | 0.16042 | 0.21473 | 0.17613
Wk-9 | 0.080556 | 0.13056 | 0.09145
Wk-10 | 0.21736 | 0.046528 | 0.08151 | 0.19949
Average | 0.076736 | 0.080492 | 0.1308 | 0.1578
Chart: MTTR SLA TREND
| Wk-1 | Wk-2 | Wk-3 | Wk-4 | Wk-5 | Wk-6 | Wk-7 | Wk-8 | Wk-9 | Wk-10
FAIL | 1 | 1 | 1 | 1 | 2 | 6 | 2 | 3
OK | 3 | 10 | 11 | 6 | 8 | 7 | 9 | 9 | 8 | 7
Average MTTR:
C-1:1:50, C-2:1:55, C-3: 3:08, No Impact: 3:47

## Slide 3
Zone Wise Incident & Outage 2019
Dhaka is most impacted in terms of Incident count and outage hour.
CTG and Mymensingh is heavily impacted as well.
Chart: ZONE WISE INCIDENT COUNT
| Dhaka North | Dhaka South | CTG | Dhaka Metro | Khulna-Barisal | Mymensingh | Comilla | Rajshahi,Kustia,Rangpur | Sylhet
Count of Incident_ID | 15 | 15 | 17 | 7 | 5 | 13 | 10 | 11 | 2
Sum of Total Outage | 64.5167 | 57.0812 | 35.8083 | 24.5917 | 19.3139 | 15.2361 | 11.8125 | 11.4014 | 2.8611
Chart: Zone wise Outage hour
| Dhaka North | Dhaka South | CTG | Dhaka Metro | Khulna-Barisal | Mymensingh | Comilla | Rajshahi,Kustia,Rangpur | Sylhet
Sum of Total Outage | 64.5167 | 57.0812 | 35.8083 | 24.5917 | 19.3139 | 15.2361 | 11.8125 | 11.4014 | 2.8611

## Slide 4
$HR++ MTTR INCIDENTS (WK09-WK10)
Week | Impact | Unit | MTTR | Link ID | Delay Reason
Wk-09 | 7 3G | SCL | 5:09:00 | SCL E2E | After fiber restore service was still down. Then engage 2nd level.
Wk-09 | 6 3G | SCL | 8:30:00 | POP: GPSRP77 | Took longer time due to stormy weather and contentious raining.
Wk-10 | 5 4G & 4 3G | SCL | 5:51:00 | GPSDR85 | 200m fiber stolen. Partner team had to lay 200 m fiber.
Wk-10 | 162 2G & 14 3G | SCL | 5:13:00 | Dhaka-2 to HUB98 and Dhaka-2 to HUB02 | Core mismatch while splicing Dhk2-Hub98.
 |  |  |  |  | Both Fibers are 432 core, restoration took longer due to higher number of cores
Wk-10 | 5 3G | SCL | 5:13:00 | BMKSB23(BB2510) | Restoration delay due to night. Incident happened at 4:16 am )

## Slide 5
C-1 Incidents-Jan’19
Week# | Date | Incident_Description | Impacted Area | ST | ET | DUR | Root Cause | Remedy Action & Plan
Wk-02 | 10-Jan | 120 3G and 14 4G sites were down | Dhaka North & Mymensingh | 3:22 | 6:08 | 2:46 | RC: Fiber- Dual Cut Link1: DH-3-HO To SCL Gazipur POP Cause: Due to fire incident at electric pole near Jajhor area, power authority cut the fiber twice FT1: 09/01 18:37 ¦¦ RT1: 10/01 6:58 ¦¦ Dur: 12:21 FT2: 10/01 09:38 ¦¦ RT2: 10/01 13:33 ¦¦ Dur: 3:55 Link2: DH-3-HO to SCL Uttara Core Cause: OH Link was down twice due to fiber cut during heavy vehicle movements. FT1: 10/01 03:12 ¦¦ RT1: 10/01 6:02 ¦¦ Dur: 2:50 FT2: 10/01 9:50 ¦¦ RT2: 10/01 10:32 ¦¦ Dur: 0:42 | RA: SCL Team restored both the fibers and lifted OH fiber to avoid risk of break due to vehicle movement. RP: SCL is building 4th OH path at new route where no construction activity going on ( 15 KM ). Time line: 17/1/19 GO redundancy of this GE will be implemented by 28th Jan 2019.
Wk-03 | 13-Jan | 55 3G sites were down | Mymensingh | 18:02 | 18:18 | 0:16 | RC: Fiber Dual Cut Link1: Uttara to Dhaka03 UG Link2: Gazipur to Uttara OH BB) Cause: R&H work and pole shifting work of REB | RA: Re-routed the traffic through different path RP: New fiber route was implemented on 18.1.19 by SCL which is more reliable as no construction activity going on.
Wk-04 | 25-Jan | 44 3G & 11 4G sites were down | CTG North | 19:29 | 19:50 | 0:21 | RC: High Loss and Fiber Cut Link1: RMMNC02 to RMSDR03 (High Loss) Link2: KCSDR04 to KCGUMA01JR01 (Fiber Cut) Cause: While doing rectification of link1, due to transformer burn link2 went down | RA: SCL team stopped high loss rectification of Link1 immediately and service became up. They restored link2 and resolved HFL of Link1 later.
Wk-05 | 31-Jan | 39 3G & 41 4G sites were down | Barisal | 0:19 | 3:50 | 3:31 | RC: CR and Configuration Error SCL Router at BHSDR03 inaccessible Due to NCR Work (Bhola SCL and TN port down or traffic checking: CRQ000000129693). Juniper router has automatic configuration rollback feature after intervals, but unfortunately it was not working. | RA: Physical configuration reset done. RP: Team presence required at site for future activities.

## Slide 6
C-1 Incidents-Feb’19
Week# | Date | Type | Incident_Description | Impacted Area | ST | ET | DUR | Root Cause | Remedy Action & Plan
Wk-06 | 5-Feb | Fiber | 33 3G sites were fluctuating & 29 4G sites were down | Mymensingh | 20:05 | 20:35 | 0:30 | RC: Fiber cut and high loss in SCL internal netwrok Cause: Sites were fluctuating due to high RSL in MNSRNB01JR01 to MNSDR07 20G. Moreover, several backbone links (DHKGN17 to NGSDRB01JR01 20G,GZ03 to Gazipur -POP, Pubail to Gazipur POP and Gazipur POP to Dhaka 3 BB) were down during that time. | RA: Re-routed the traffic to another route to resolve this issue. RP: High loss was resolved as well as backbone fiber cuts were restored.
Wk-06 | 6-Feb | Fiber | 13 2G, 52 3G & 11 4G sites were down | CTG North | 14:58 | 15:52 | 0:54 | RC: Fiber dual cut POP:KCSDR04, RMBGC05,KCDGN01 & CGFTK23 Link1: RMMNC02 to RMSDR03 Cause: OH fiber cut by local people (cable TV operator). FT: 14:19 ¦¦ RT: 15:49 ¦¦ DUR: 01:30 Link2: KCGUMA01 to CGHTZ18 Cause: Due to core broken inside tj box FT: 14:52 ¦¦ RT: 16:57 ¦¦ DUR: 2:05 | RA: Link1 pulled up & spliced. Link2 core rectified inside tj box. RP: OH Cable height increased & fixed it properly.
Wk-08 | 17-Feb | Fiber | 38 3G and 59 4G sites were down | Dhaka Metro | 2:48 | 2:59 | 0:11 | RC: Dual Fiber Impact Link1: High loss at Dhaka1--HUB98 of Hamida OSN link: DH0325--Dhaka1--HUB98 for lambda connectivity Cause: High loss FT: 16/02 23:52 ¦¦ RT: 17/02 02:59 ¦¦ DUR: 03:07 Link2: SCL team plug out fiber from HUB98 end of WDM link: DH0325—HUB98 to rectify high loss resulting impact. Cause: Fiber plug out from SCL path but High Loss was in Hamida path caused the impact. FT: 02:48 ¦¦ RT: 02:59 ¦¦ DUR: 00:11 | RA: Fiber Restored by plug in the right patch cord at ODF. RP: The incident has been recorded as and learning case. For further issues with the OSN link TX Ops to be consulted before unplugging ODF.

## Slide 7
Quality Issues on 01-Jan to 09-Mar,2019 (SCL)
Month | No of Incidents | Sum of Node Count | Sum of Non quality hours
Jan'19 | 8 | 353 | 1363
Feb'19 | 2 | 107 | 604
Mar'19(Till 9th Mar) | 2 | 76 | 896
Grand Total | 12 | 536 | 2863
Chart: Incident Count vs Impacted Node
| Jan'19 | Feb'19 | Mar'19(Till 9th Mar)
Sum of Node Count | 353 | 107 | 76
No of Incidents | 8 | 2 | 2
Chart: Incident Count vs Non Quality Hours
| Jan'19 | Feb'19 | Mar'19(Till 9th Mar)
Sum of Non quality hours | 1363 | 604 | 896
No of Incidents | 8 | 2 | 2
5 Incidents in Gazipur impacting 300 Nodes in total.
2 incidents repeated at Gazipur : 10GE_SCL_DRE14_DRH19_DRH21_DRE29_GPSDRO5_GPSDR34_102 & 3G_4G_2X10GE_SCL_DRE14_DRH19_DRH21_DRE29_DRE35_GPSDRO5_DHGULO1_184

## Slide 8
Quality Issues on Jan-2019 (SCL)
Incident Date | Impact | Tx Owner | GE/POP | Resolution | Duration
14/1/2019 | HS Frame Loss: 54 Node B | SCL | GE: 3G_4G_10GE_SCL_DRE14_DRH19_DRH21_DRE29_GPSDRO5_GPSDRI1_113 | Resolved by SCL | 4:46:13
14/1/2019 | HS Frame Loss: 89 Node B | SCL | GE: 10GE_SCL_DRE14_DRH19_DRH21_DRE29_GPSDRO5_GPSDR34_102 | Resolved by SCL | 4:31:38
14/1/2019 | HS Frame Loss: 81 Node B | SCL | GE: 3G_4G_2X10GE_SCL_DRE14_DRH19_DRH21_DRE29_DRE35_GPSDRO5_DHGULO1_184 | Resolved by SCL | 4:11:19
20/1/2019 | Ping Loss: 7 Node B | SCL | PoP: Fenchuganj | Resolved by SCL | 0:22:20
22/1/2019 | High Call Drop: 223 Cells | SCL | GE: 3G_4G_10GE_SCL_DRE03_DRE11_DRE15_DRE28_DRE37_NGRPG01_NGSDRD1_179, 3G_4G_2X10GE_SCL_DRE03_DRE11_DRE15_DRE28_NGRPG01_DHPTN42_111 | Resolved by SCL | 0:58:19
22/1/2019 | High Ping Loss: 81 Node B | SCL |  | Resolved by SCL | 1:46:14
23/1/2019 | Ping Loss: 10 Node B | SCL | PoP: pirojpur | Problem solved from 2019-01-23 11:09:37 BDT. Root Cause - several BB down at Bagerhat area. | 2:28:20
28/1/2019 | High Ping Loss: 8 Node B | SCL |  | Below problem was occurred due to high RSL at DPPBT03 to DPPBT02 link. | 21:15:28

## Slide 9
Quality Issues on Feb-2019 (SCL)
Incident Date | Impact | Status | Tx Owner | GE/POP | Resolution | Duration
11/2/2019 | High call drop: 153 Cells | Closed | SCL |  | SCL TX issue | 3:15:52
20/2/2019 | Fluctuation: 654 Cells | Closed | SCL |  | Found resolved. RCA will share after getting from SCL | 6:11:37
Quality Issues on Mar-2019 (SCL), Till 9th March
Incident Date | Impact | Status | Tx Owner | GE/POP | Resolution | Duration
4/3/2019 | HS Frame Loss: 46 Node B | Resolved | SCL | GE: 3G_4G_2X10GE_SCL_DRE14_DRH19_DRH21_DRE29_DRE35_GPSDRO5_DHGULO1_184 | Resolved by reroute. RCA will share by mail | 19:12:21
6/3/2019 | HS Frame Loss: 30 Node B | Resolved | SCL | GE: 3G_4G_10GE_SCL_DRE14_DRH19_DRH21_DRE29_GPSDRO5_GPSDR34_102 | Issue found resolved previously. RCA will share after getting from SCL. | 0:24:28