## Slide 1
Weekly NTTN Governance Meeting
Wk-15

## Slide 2
MoM
SL # | Agenda | Discussion | Status | Responsible Team | Issue Raising Date | Issue fixing date
1. | Database of Site Dependency on POP/ GE / Dark cores | SCL requires Site dependency list on each POP/Base Site, GE & Dark Core connectivity. Robi will check and will provide us required informations. | Open | Robi | 12/02/2019 | N/A
2. | Weekly meeting format update | Weekly presentation format needs to be updated | Open | Robi & SCL | 09/04/2019 | 

## Slide 3
Availability Trend (3G Site)
Availability Threshold | Color Coding
99.95% to 100% | Green
99.90% to 99.95% | Yellow
Below 99.90% | Red
Week | Duration (hh:mm) | Site Down | MTTR (hh:mm) | Weekly Availability(%)
Week 12 | 106.25 | 19 | 5.59 | 99.99
Week 13 | 105.99 | 28 | 3.79 | 99.99
Week 14 | 446.53 | 64 | 6.98 | 99.96
Week 15 | 109.89 | 37 | 2.97 | 99.99
Chart: Zone Wise Outage_Wk 15
| DHAKA | CHANDPUR | CHITTAGONG | GAZIPUR | JAMALPUR | JHENAIDAH | MUNSHIGANJ | NARAYANGANJ
Count | 9 | 2 | 2 | 2 | 1 | 1 | 1 | 1

## Slide 4
Weekly Incident trend
Chart: Incident Count Trend (C1, C2 & C3
| Wk-01 | Wk-02 | Wk-03 | Wk-04 | Wk-05 | Wk-06 | Wk-07 | Wk-08 | Wk-09 | Wk-10 | Wk-11 | Wk-12 | Wk-13 | Wk-14 | Wk-15
Count | 13 | 17 | 25 | 25 | 21 | 25 | 23 | 34 | 39 | 25 | 20 | 22 | 22 | 35 | 30
Average Incident Count | 25.0667 | 25.0667 | 25.0667 | 25.0667 | 25.0667 | 25.0667 | 25.0667 | 25.0667 | 25.0667 | 25.0667 | 25.0667 | 25.0667 | 25.0667 | 25.0667 | 25.0667
Chart: MTTR Trend (SCL Base Site)
| Wk 1 | Wk 2 | Wk 3 | Wk 4 | Wk 5 | Wk 6 | Wk 7 | Wk 8 | Wk 9 | Wk 10 | Wk 11 | Wk 12 | Wk 13 | Wk 14 | Wk 15
MTTR | 2.1029 | 2.378 | 0.851 | 1.3197 | 2.382 | 2.3063 | 2.6963 | 4.6518 | 3.6959 | 2.7969 | 4.3851 | 5.5923 | 3.7853 | 6.977 | 2.9699
Average | 3.2594 | 3.2594 | 3.2594 | 3.2594 | 3.2594 | 3.2594 | 3.2594 | 3.2594 | 3.2594 | 3.2594 | 3.2594 | 3.2594 | 3.2594 | 3.2594 | 3.2594
Chart: Outage hour Trend (SCL Base Site)
| Wk 1 | Wk 2 | Wk 3 | Wk 4 | Wk 5 | Wk 6 | Wk 7 | Wk 8 | Wk 9 | Wk 10 | Wk 11 | Wk 12 | Wk 13 | Wk 14 | Wk 15
Outage Hours | 67.2917 | 104.63 | 135.3086 | 112.1747 | 123.8644 | 66.8833 | 124.0306 | 181.4211 | 133.0508 | 75.5158 | 153.4786 | 106.2528 | 105.9897 | 446.5275 | 109.885
Average | 136.4203 | 136.4203 | 136.4203 | 136.4203 | 136.4203 | 136.4203 | 136.4203 | 136.4203 | 136.4203 | 136.4203 | 136.4203 | 136.4203 | 136.4203 | 136.4203 | 136.4203

## Slide 5
Ongoing Network Improvement Activity
Priority-1
390 Links PM already done within 15-Apr-19
Priority-2
138 Links PM WIP
Preventive Maintenance
Network Swap
Priority-1:
Total 532 sites swap done
2 site (MNSRN18, RJGLN01) remaining due to ROBI site access issue.
Priority-2:
70 out of 70 sites done
Link Shifting from OH to UG fiber
Total Target: 131 links (~1,968Km fiber)
Shifting Done: 4 links (~120 km fiber)
Deadline: 31-May-19
Capacity Upgradation
BB & AGG Links:
  10G to 100G: 3 Links
  20G to 30G: 2 Links
  10G to 20G: 7 Links
  1G to 10G: 2Links
  New 10G: 4 Links
  1G to 2G: 1 Links
Access Links:
  1G to 10G: 459 Links
Chart: 
| Already Done | W-17 | W-18 | W-19 | W-20 | W-21 | W-22
Shifting Target (Link) | 4 | 7 | 10 | 20 | 25 | 30 | 35
Cumilitive Total (Link) | 4 | 11 | 21 | 41 | 66 | 96 | 131

## Slide 6
BB Link Capacity Upgradation
SL | Link Names | Capacity | Status | Date | Remarks
1 | Gazipur POP to Pubail-HO | 10G to 100G | Done | 13-Mar-19 | 100G ring Uttara-Pubail-Gazipur-Savar-Mirpur.
2 | Pubail-HO to Uttara POP | 10G to 100G | Done | 13-Mar-19 | 
3 | Pubail HO to DH03_HO to Gazipur POP | 20G to 30G | Done | 5-Apr-19 | 
4 | Gazipur-Mawna-Mymensingh Backbone | 10G to 20G | Done | 24-Mar-19 | 
5 | DHKGN17 to DHNWG04 | 10G to 20G | Done | 11-Apr-19 | 
6 | MNSRN18 to Srinagar POP | 10G to 20G | Done | 11-Apr-19 | 
7 | Savar POP -- GPKLK66 -- GPKLK04 -- Gazipur POP | 10G | Done | 27-Mar-19 | New 10G ring established
8 | MYSDR03 - MYPGCB link up-gradation | 1G to 2G | Done | 25-Mar-19 | 
9 | TNMZP46 - TNMZP08 New Link | 10G | Done | 27-Mar-19 | 
10 | DHKGN17 -- Paltan POP | 10G to 100G | Done | 9-Apr-19 | Keraniganj/Nawabgabj is now connected with 100G BB
11 | Working and protection path separation for Dhaka2-HUB02 | Dark core link | Done | 12-Apr-19 | 
12 | JPSDR28-JPMDG02 | 1G to 10G | Done | 5-Apr-19 | 
13 | JPSDR28-MYPGCB | 1G to 10G | Done | 5-Apr-19 | 
14 | JPSDR02-JPMDG02 | 1G to 10G | Not Done |  | Dependency: ROBI could not arrange access at JPSDR02 site
15 | Tongi Station Road- Uttara House Building new fiber route | - | WIP | 15-Apr-19 30-Apr-19 | Deadline Missed

## Slide 7
Focus on Dhaka Metro Network
Dhaka Metro Network Improvement Activity
• Working and protection path separation for Dhaka2-HUB02
• Continuous communication with R&H,PDB,WASA, authority & contractors
• Preventive Maintenance
• Engineers presence all the time at field during the Gov. activities
• Regular patrolling to prevent BB Damage
UG BB Fiber Saved During Gov. Activity Without any Outage
Bijoy Nagar HDD Work of WASA
Press Club HDD Work of WASA
Drainage Activity Malibag to Rampura Route of Wasa
Hamida HDD work at Satrasta
Kadam Chattar to Dohar
Baksi Bazar DPDC activity
Dhalpur Wasa Drainage Activity
Current Patrolling Area to Protect BB Fiber
Paribag, Rampura, Malibag and Peripheral area of KBZ SC
Gazipur Chowrasta to Vogra By Pass Tongi
Uttara Airport Tongi Area
Mirpur MRT Hdd Work & Agargaon Area
Moghbazar BTCL and baily road.

## Slide 8
Repetitive Incident Link Rectification Status
Action Plan Summary | Solved | WIP
Increased fiber height and properly fixed to pole | 10 | 2
Install new pole to increase cable height. | 1 | 0
Preventive Maintenance | 21 | 51
Patrolling for On-going Gov. Activity | 4 | 28
Fiber Reroute | 1 | 1
High Loss Rectification | 1 | 0
Ring Modification | 0 | 1
Hill Tract Dependency (Clearing the jangol) | 0 | 1
OH to UG Shifting | 10 | 8
SFP Replaced | 1 | 0
Total | 49 | 92
Grand Total | 141 | 
Repetitive Link Down Analysis
• Total 236 links Identified for last 3 months
• Priority 141 links identified where 49 links already solved and 92 links WIP

## Slide 9
SCL Dark Core Fibers Contributed to C-1 Incident
Chart: Dark Core Avaliability (Dec'18-Mar'19)
| Hub10 to DH0126 | HUB_10 to HUB_14 | DH0075 to HUB_06 | DHMRPB4 (HUB_14) to DHKFR58 (DH0019) | DHMRPB4(HUB_14) to DHADB44(HUB_18) | DHKDM42 (DH0075) to NGSDRJ1 (NG2138) | DHKDM30(DH0076) to DHSTR68(DH0285) | DHLLB50(DH0164) to DHSTR68(DH0285) | DHMRPB4 (HUB_14) to DHSVRJ9 (DH0032) | Dhaka-2 to HUB98 | Dhaka-2 to HUB02 | MG2121 to NG2136 | DHKDM42(DH0075) to DHKDM30(DH0076)_DWDM | DHKDM42(DH0075) to DHKDM30(DH0076)_OSN | DHPTN42(Dhaka_2) to DHICX02(Borak) | DHPTN42(Dhaka_2) to DHRMN72(DH0502) | DHTIA53(DH0705) to DHRMP53(HUB_05) | NGBND30(NG2110) to NGSDRJ1(NG2138)
Achive | 1 | 1 | 1 | 1 | 1 | 1 | 0.98655 | 0.99086 | 0.99654 | 0.98976 | 0.97889 | 0.99132 | 0.98887 | 0.99721 | 0.99387 | 0.9858 | 0.99886 | 0.98402
Traget (99% Yearly) | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99
ROBI Complain for 13 Dark Core Links
• Six (6) links have 100% availability for last 4 months
• Three (3) links were down and meet SLA for last 4 months
• Three (3) links repetitively down and could not meet SLA for last 4 months
• One (1) link is not under SCL
• In addition, there were another six (6) links which were down repetitively.

## Slide 10
SCL Dark Core Fibers Contributed to C-1 Incident
SL | Dark Core Link Name | Fault Reason | Remedy Plan
1 | Dhaka-2 to HUB02 | • UG Backbone 432F damaged at Paribagh due to HDD activity by Hamida Traders Ltd (Vendor BdREN) • Enclosure damaged at Malibag Maxim HH due to DNCC drainage activity. • UG Backbone shifting at Poribagh BTCL • UG Backbone 144F damaged at Sahabag | • Working and protection path separation done • 24/7 Patrolling ongoing.
2 | DHKDM30(DH0076) to DHSTR68(DH0285) | • Fiber high bend at 95 Bou Bazar Shympur | • PM Activity WIP
3 | Dhaka-2 to HUB98 | • Enclosure damaged at Malibag Maxim HH due to DNCC drainage activity. • UG Backbone damaged at Near Mama Vagna POC | • 24/7 Patrolling ongoing.
4 | DHKDM42(DH0075) to DHKDM30(DH0076) SCL DWDM | • Core bend inside TJ • Fiber Burnt at Sonir Akhra & Zia Soroni Road due to transformer bluest | • PM Activity WIP
5 | DHPTN42(Dhaka_2) to DHRMN72(DH0502) SCL DWDM | • UG 144F damaged near Rajmoni Cinema hall kakrail due to HDD activity by WASA | • 24/7 Patrolling ongoing.
6 | NGBND30(NG2110) to NGSDRJ1(NG2138) SCL OSN | • Fiber cut by Gov. tree decluttering activity • Fiber cut during Govt. Road expansion activity | • PM Activity WIP
NB: Dark Core List with Working and Protection Info Required from ROBI

## Slide 11
Repeated Site Down for Robi Power Issue
Site Code | Week 12 | Week 13 | Week 14 | Week 15
DHMDP77 | 2 | 9 | 9 | 5
CXCKR60 | 1 | 9 | 5 | 8
Shatkhira_WIC | 7 | 3 | 6 | 6
Laxmipur-WIC | 6 | 0 | 5 | 8
DHUTK12 | 3 | 4 | 6 | 2
MBBRL23 | 1 | 0 | 7 | 5
KSKLC08 | 1 | 1 | 5 | 3
MBBRL22 | 0 | 4 | 2 | 4
SYDKS30 | 1 | 0 | 4 | 4
MBSDR02 | 1 | 0 | 6 | 1
CXRMU29 | 0 | 1 | 4 | 2
GPSDR09 | 0 | 3 | 2 | 2
CMDBD39 | 1 | 0 | 2 | 4
DHBDD98 | 1 | 2 | 2 | 1
DHSTR12 | 0 | 2 | 2 | 2
GPSDR55 | 1 | 0 | 3 | 2
BSWZP18 | 1 | 1 | 2 | 2
NGSDR45 | 0 | 0 | 4 | 2
MGSBL04 | 0 | 2 | 2 | 2
SYFNC16 | 0 | 0 | 3 | 3
BMNBG29 | 0 | 0 | 6 | 0
CMCDG34 | 0 | 1 | 4 | 1
DHDKK15 | 0 | 4 | 0 | 2
DHKGN18 | 0 | 0 | 2 | 4
DHLLB16 | 0 | 2 | 0 | 4
DHRMN40 | 0 | 1 | 1 | 4

## Slide 12
Issue Dependency on ROBI
CI & C2 Site list along with child site info wouldn’t shared with SCL. [Deadline was 15-Apr-19]
6 Hill Tracts site’s are unprotected due to ROBI MW link dependency. [Deadline was 15-Apr-19 for Exaction Plan]
Dark Core List with Working and Protection Info Required from ROBI

## Slide 13
Impact | GE/POP | Reason | Resolution/ Remedy Plan | Start Date
High Ping Loss in 9 Node-B Under DRH19 | KS1853 | We have observed that utilization is 400 mb for mentioned service and to mitigate this problem, capacity needs to increased. Currently we have device capacity dependency to execute up-gradation. In this circumstances planning level communication required between Robi and SCL. | Device Installation Done. | 3/31/2019 14:41
HS frame loss under FNSDR35 POP | FNSDR35 | We are not getting any problem at our TX. | Traffic has been re routed as per Robi request | 4/4/2019 10:14
HS Frame Loss in 77 Node-B Under RRH22 | 3G_4G_2X10GE_SCL_RRH22_NTSDR02_55 and 3G_4G_GE_SCL_RRH22_NTSDR02_02 | Due to sudden traffic overflow issue occurred. | Traffic has been re routed | 4/10/2019 13:07
DCH frame loss in DHMRP28 | DHMRP28 | High loss in DHMRP12 to Uday-HO path | High loss has been reduced | 4/11/2019 6:48
HS Frame Loss in 15 Node-B Under DRE35 | GPSDR15 | Root cause identification is ongoing | NA | 4/10/2019 12:51
HS Frame Loss in 77 Node B Under DRE37,HS Frame Loss in 77 Node B Under DRE37 | 3G_4G_10GE_SCL_DRE03_DRE11_DRE15_DRE28_DRE37_NGRPG01_NGSDRD1_179,NA,3G_4G_2X10GE_SCL_DRE03_DRE11_DRE15_DRE28_NGRPG01_DHPTN42_111 | Backbone link problem at MNSRNB01JR01 to MNSRN18 | MNSRNB01JR01 to MNSRN18 link has been upgraded to 20G | 4/9/2019 10:26
Quality Issues on week-14 (SCL)

## Slide 14
C1 C2 Feedback
Wk | Incident | Start Time | End Time | Outage Duration | Link Info/ POP Info | Root Cause | Action Taken | Remedy Plan
Wk 15 | 17 Node B under DRE35,DRE10 and 10 eNode B are down since 07:29 | 4/8/19 7:29 AM | 4/8/19 10:45 AM | 3:16:00 | GPSDR37,GPKLK04 | There was power issue at the GPKL04 site. Also fiber was cut in another hand of the ring. | Fiber pulling was completed and splicing was done in order to restore the link | New Fiber pulling done and regular PM is needed to avoid this kind of situation.
Wk 15 | 16 Node B under DRE35,DRE10 and 10 eNode B are down since 13:09 | 4/8/19 1:09 PM | 4/8/19 4:33 PM | 3:24:00 | GPSDR37 | There was fiber cut in both hands. One hand was cut due to storm and another one was cut due to BRT regular activity. | In two hand, fiber deployment was done. | New Fiber pulling done and regular PM activity is suggested.
Wk 15 | 18 Node B under DRE15 and 23 eNode B are down since 14:19 | 4/9/19 2:19 PM | 4/9/19 11:30 PM | 9:11:00 | DHSTR68(DH0285) to NGSDRG3(NG2136) SCL | There was fire broke out in Postogola Bridge, that’s why fiber was burnt | After complain found team moved and checked the link after Postogola rail crossing and found both core break toward Postogola bridge . team arrived at incident place and found fiber burn due to electric short circuit near Postogola bridge .Here DPDC team not allowing anyone to work for the sake of safety . Also due to rain work stopped by DPDC . After rain DPDC team start work . after dpdc team completed their work ,scl team allowed to work and fiber restored . | As fiber was damaged by electric burn , we deployed new fiber by maintaining a safe distance from electric line .
Wk 15 | DHSTR68(DH0285) to NGSDRG3(NG2136) DWDM fiber is down since 04:20 + 18 Node B under DRE15 and 23 eNode B are down | 4/10/19 4:20 AM | 4/10/19 5:17 AM | 0:57:00 | DHSTR68(DH0285) to NGSDRG3(NG2136) | We have 144 core fiber in the link for backbone. It was damaged partially by storm. That’s why link was down. | The mentioned link was the first priority and our team spliced this link’s core first and made the link restored. | Regular PM activity is suggested for reqular maintenance and avoid such disaster.
Wk 15 | 9 Sites under CBEB2, 29 Node B under CRE25,DRE12 and 15 eNode B are down since 05:24 | 4/13/19 5:24 | 4/13/19 11:05 | 5:41:00 | KCDGN01,RMBGC05,RMLND01 | Fiber was cut in the two hands of the ring that is why down incident occurred | Fiber was deployed to up the link . | Regular PM activity is suggested for reqular maintenance and avoid such disaster.

## Slide 15
More Than 4hrs of Site Down
Site | Event Time | Clear Time | Duration | Remarks
NSPLS02 | 4/12/2019 12:52 | 4/12/2019 22:58 | 10.10 | Fiber cut by sabotage issue. Several places fiber cut.
FPSDR42, FPSDR26 | 4/11/2019 2:13 | 4/11/2019 8:59 | 6.75 | Fiber cut near anather mor
DHKGN33 | 4/9/2019 14:45 | 4/9/2019 20:24 | 5.65 | Both hand fiber was cut for heavy strom at Keraniganj
GPSDR55 | 4/11/2019 11:31 | 4/11/2019 17:08 | 5.61 | Fiber cut by miscreant
GPSDR37, GPSDR09,GPSDR49, GPSDR22, GPSDR40, GPSDR11 | 4/8/2019 13:10 | 4/8/2019 18:18 | 5.14 | One hand is down due to pole shifting and another hand is down due to road expansion.
DHJTB13 | 4/8/2019 14:36 | 4/8/2019 19:37 | 5.02 | Fiber cut at Matuail Union paraishad
DHKHL17, DHKHL18 | 4/8/2019 3:21 | 4/8/2019 8:20 | 4.98 | Single core break near vertical
JSSDR13 | 4/9/2019 9:45 | 4/9/2019 14:40 | 4.91 | Site was down due to UG fiber cut at Jashore Airport area. Fiber was cut due to Airport runway expansion work.
DHSHM01 | 4/11/2019 5:43 | 4/11/2019 10:12 | 4.48 | Both hand down due to fiber cut. Location: KB road

## Slide 16
More Than 6hrs of Dark Core Link Down
Link Name | Event Time | Clear Time | Duration | Reason
DHBDDC8(HUB98) to DHPTN42(Dhaka_2) | 4/6/19 6:56 PM | 4/7/19 6:20 AM | 11:14:00 | Both core break after 24 meter towards building solution cable.
GPSDR34(Pubail) to GPSDRP3(GP1626) | 4/7/19 1:36 AM | 4/7/19 11:24 AM | 9:34:00 | Fiber damaged due to heavy storm.
DHICX02(Borak) to DHRMN03(Moghbazar) and DHICX02(Borak) to DHMJH28(Twin tower) | 4/8/19 2:51 AM | 4/8/19 7:07 PM | 15:49:26 | SCL Underground 144 core backbone was damaged at Mogbazar.
DHSTR68(DH0285) to NGSDRG3(NG2136) | 4/9/19 2:09 PM | 4/9/19 11:25 PM | 9:03:00 | Backbone fiber burnt due to electric short circuit near Postogola bridge. Team faced work restriction from Govt. authority. Alsoteam had to change the damaged fiber portion.
DHKFR58(DH0019) to DHMRPB4(Hub_14) | 4/9/19 6:02 PM | 4/10/19 1:38 AM | 7:19:00 | Core break inside TJ box at DGFI POC. Rectification work delayed due to access and work restriction at Cantonment area.

## Slide 17
Repetitive Link Name | Zone Name | Repetitive Count |  |  |  | Reason | Action/ Remedy plan | Start date | Target date to fix
 |  | Wk 12 | Wk 13 | Wk 14 | WK 15 |  |  |  | 
CT3323 to CT3421 | Chittagong | 1 | 1 | 0 | 1 | There was road expansion work by govt authority in Halishahar area. That is why Link was Down. | One time was stand by on spot to reduce the downtime. The team pulled fiber and made the link up. | 3/17/2019 | 
DH0285 to NG2136 | Narayanganj | 0 | 1 | 0 | 2 | Problen In ROBI End. |  | 3/30/2019 | 
NG2138 to NG2110 (Protection) | Narayanganj | 1 | 1 | 0 | 1 | Due to the decluttring activity by Govt authority, fiber was cut. | 250 meter new fiber was pulled in order to make the link restore. | 3/17/2019 | 
Repeated Dark core(Robi) Breaks-Weekly

## Slide 18
Thank
You